## Slide 1: Convolutional Neuronal networks Practice part

## Slide 2: 1. Lab roadmap
Learning objectives of this chapter:
  You know the different projects that you will carry out during the lab
Frame conditions of this project
  Requires roughly 60 hours of work
  You will deal with the following topics:

## Slide 3: 2. Software set up
Learning objectives of this chapter:
  You know which programs and accounts are needed for the project
  You installed and set up all important platforms
The diagram below shows which platforms are necessary

## Slide 4: 2. Software set up
Task: Please set up the platforms in the table below
Platform | Platform address | Account needed? | Download needed?
WinSCP | https://winscp.net/eng/download.php | No | Yes
VNC Viewer | https://www.realvnc.com/de/connect/download/viewer/ | No | Yes
PuTTY | https://www.putty.org/ | No | Yes
Arduino | https://www.arduino.cc/en/main/software | No | Yes
Anaconda prompt | https://www.anaconda.com/products/individual | No | Yes
Git | https://git-scm.com/downloads | No | Yes
GitHub | https://desktop.github.com/ | Yes | No
Google Colab | https://colab.research.google.com/notebooks/intro.ipynb | Yes | No

## Slide 5: 2. Software set up
Why is it necessary to install and set up some programs and accounts?
  WinSCP; VNC viewer: needed to transfer data between your computer and the local computer of the truck (the Raspberry Pi)
  PuTTY: is the console of WinSCP and is needed to send commands to the Raspberry Pi
  Arduino: needed to make adaptions at the Arduino Nano that controls the traffic lights
  Anaconda prompt: will be needed for data set creation
  Git, GitHub,
  Google Colab: are needed for some exercises and the truck project

## Slide 6: 3. Simple neural network creation
Learning objectives of this chapter:
  Neural network skills:
    You can set up your own neural network
    You can establish your approach at the neural network creation
    You can explain your neural network to others
  Software skills:
    You know how to save a trained network
    You can set up a connection between Colab and GitHub
    You can unzip files in the network

## Slide 7: 3. Simple neural network creation
Task:
  Set up a neural network that is able to distinguish between different types of clothes
  Use the fashion MNIST data set
  The accuracy should be at least 90%
  The data set contains 60.000 training pictures and 10.000 test pictures

## Slide 8: 3. Simple neural network creation
For the creation of a neural network follow the described steps. A detailed description is available in chapter 3 of the script.

## Slide 9: 3. Simple neural network creation
3.1 GitHub set up
  Create a GitHub folder structure for the repository
  Then load the fashion MNIST data set into the repository
3.2 Neural network environment
  environment set up includes:
    installation of basic libraries
    cloning and forking the repository
    implementation of the data set
  The single process steps are described in the next section
[1]
[2]

## Slide 10: 3. Simple neural network creation
3.2.1 Installation of basic libraries
  Install the basic libraries as for example TensorFlow or NumPy
  Helpful additions:
    !pip install --upgrade deeplearning2020
    from deeplearning2020 import helpers
    import gzip
    !pip install h5py pyyaml
    from_future_importabsolute_import, division, print_function

## Slide 11: 3. Simple neural network creation
3.2.2 Fork and clone the repository
  Clone it in order to access it
  Clone your own repository to be able to work with it
  Clone other repositories to work with their codes, data, and results
  Example:
    # Forked repository
    repo_url = 'https://github.com/MariusLandmann/SmartSystems_CNN_TrafficLightDetection'
    #Clone repository
    import os
    %cd /content
    repo_dir_path = os.path.abspath(os.path.join('.', os.path.basename(repo_url)))
    !git clone {repo_url}
    %cd {repo_dir_path}
    print('Pull it so that we have the latest code/data')
    !git pull

## Slide 12: 3. Simple neural network creation
3.2.3 Load the data set
  Load the data set to the environment of your neural network
  Do not forget to unzip compressed data
  Example:
with gzip.open(images_path, 'rb') as imgpath:
images = np.frombuffer(imgpath.read(), dtype=np.uint8,
offset=16).reshape(len(labels), 784)
return images, labels
#Loading the data with Python
X_train, y_train = load_mnist('dataset_FASHION', kind='train')
X_test, y_test = load_mnist('dataset_FASHION', kind='t10k')
# X: images; y: labels
#mnist_reader
def load_mnist(path, kind='train'):
"""Load MNIST data from `path`"""
labels_path = os.path.join(path,
'%s-labels-idx1-ubyte.gz'
% kind)
images_path = os.path.join(path,
'%s-images-idx3-ubyte.gz'
% kind)
with gzip.open(labels_path, 'rb') as lbpath:
labels = np.frombuffer(lbpath.read(), dtype=np.uint8,
offset=8)
1
2

## Slide 13: 3. Simple neural network creation
  Follow the described steps
  Reshape, shuffle, and normalize the pixel values
  Convert the labels to a vector if necessary
  Create a basic layer structure for your neural network
  Test different optimizers and chose the best fitting one
  Train your neural network in 12 epochs
  Evaluate the network with your test data set

## Slide 14: 3. Simple neural network creation
3.4 Save the neural network
  Save it in your cloned repository
  Example saving:
  Recreate the network if necessary
  Example recreating:
3.5 Save the data in your GitHub repository
  Download the previously saved model into your locally created repository
  Afterwards push it
  Example for download:
model.save('./trained_CNN/fashion_MNIST/my_model_adam.h5')
#Recreate whole model
new_model=keras.models.load_model('./trained_CNN/fashion_MNIST/my_model_adam.h5')
new_model.summary()
# DOWNLOAD created files (in this case the model created previously)
from google.colab import files
files.download('./trained_CNN/fashion_MNIST/my_model_adam.h5')
# Push Anzeigen -> Inhalt -> files can display everything that download all generated

## Slide 15: 3. Simple neural network creation
3.6 Unzip a data set
  Download the data set from the repository (https://github.com/MariusLandmann/SmartSystems_CNN_TrafficLightDetection/tree/master/dataset_FASHION/in_csv) to your local workspace
  Then load it to your repository
  Unzip the compressed data in Colab
  Example for unzip:
# Unzip CSV data and assign a variable to it
import zipfile
with zipfile.ZipFile('/content/SmartSystems_CNN_TrafficLightDetection/dataset_FASHION/in_csv/train_compressed_fashion-mnist_train.csv.zip', 'r') as zip_ref:
zip_ref.extractall('/content/SmartSystems_CNN_TrafficLightDetection/dataset_FASHION/in_csv')
train_csv='/content/SmartSystems_CNN_TrafficLightDetection/dataset_FASHION/in_csv/fashion-mnist_train.csv'
#!cat {train_csv}

## Slide 16: 4. Simple CNN creation
Learning objectives of this chapter:
  You can set up your own CNN
  You can establish your approach at the CNN creation
  You can explain your CNN to others
  You can integrate a data set in Colab
  You know how to save a trained network

## Slide 17: 4. Simple CNN creation
Task:
  Set up a neural network that is able to distinguish between ten different dog breeds
  Use the fashion ImageWoof data set
  The accuracy should be at least 50%
  At first you should download the data set from deeplearning2020 and integrate it in Colab.
  Example:
  !pip install --upgrade deeplearning2020
  from deeplearning2020.datasets import ImageWoof
  train_data, test_data, classes= ImageWoof.load_data()

## Slide 18: 4. Simple CNN creation
Follow the described steps for the creation of a neural network. For a detailed description look into the task you have done before.

## Slide 19: 4. Simple CNN creation
After the CNN was created answer the following questions:
  What are the main differences in the layer structure between the exercises of chapters 3 and 4?
  Which CNN is faster?
  Why is one CNN faster than the other?
  What had the most influence on increasing the accuracy of the CNN?
  Were there any surprising findings for you? If yes, which ones?
  Which part was most problematic for you?

## Slide 20: 5. Truck project
Learning objectives of this chapter:
  You can explain the “Smart Truck” project that will be implemented during the laboratory sessions
  You know the hardware and software design of the truck
  You can explain how to set up a connection between your computer and the truck (Raspberry Pi)

## Slide 21: 5. Truck project
5.1 Introduction to the truck project
Smart Truck CNN task
  Detection of the traffic light and the correct colour.
  Action according to the traffic light status (e.g. stop at red, start/continue at green)
Possible traffic light status
Task:
  Please read chapters 1 till 2.2 in the “Smart Truck Manual” for more detailed instructions to the truck itself

## Slide 22: 5. Truck project
5.2 First truck connection
Task:
    Please read the description in the “Smart Truck Manual” in chapter 3.1 and set up the connection between the Raspberry Pi and your computer

## Slide 23: 6. Data set creation
Learning objectives of this chapter:
  You can explain and set up the single steps that are necessary to create a data set
  You can explain and justify the requirements of a proper data set

## Slide 24: 6. Data set creation
Task:
  Create your own data set by following the given instructions. The data set should contain 300 pictures of the traffic light that will be used in the project.
6.1 Image creation
  take images of the things that should be identified
  use the same device as in the truck project
  use a special program for the Arduino Nano (each colour interval should have a duration of 10 seconds)
  follow the Arduino Nano change instructions (6.1.2) to set the longer interval
  follow the instructions for image taking (6.1.2)

## Slide 25: 6. Data set creation
6.1.1 Changing the Arduino Nano program
  Open Arduino IDE
  Configure as follows (just at the first time necessary):
    Open the tab “Werkzeuge”
      Chose the category “Board” and set Arduino Nano
      Chose the category “Prozessor” and set ATmega328P (Old Bootoloader)
      Chose the category “Port” and set COM4
      Chose “Programmer” and set USBap
  Now open the code “traffic_light_image” that you want to load to the Arduino Nano

## Slide 26: 6. Data set creation
6.1.1 Changing the Arduino Nano program
  Now push the arrow in the circle to transfer the code to the Arduino Nano
  Follow the same process to transfer the original program “traffic_light” back to the Arduino Nano

## Slide 27: 6. Data set creation
6.1.2 Image taking
  Open the program “take pictures” with the VNC viewer
  A picture always gets taken if you push space
  Take pictures of each phase for each set up to get a balanced data set
  Get a high variety of pictures:
    take different picture backgrounds and image sections
     traffic light in the middle/left/right
    take pictures at different light conditions
     light from the front/side/back and different light conditions
    as daylight/twilight/night light

## Slide 28: 6. Data set creation
6.2 Image labelling
Tasks:
  Install “labelimg” with support of the process description (6.2.1)
  Label the images with “labelimg” (6.2.2)

## Slide 29: 6. Data set creation
6.2.1 Install labelimg
  Install “labelimg” with support of the process description in the script (6.2.1)

## Slide 30: 6. Data set creation
6.2.2 Label with labelimg – program overview
  1 – Open a new image
  2 – Save the labelled image
  3 – Chose the storage format (VOC)
    VOC is used if the label should be a xml file
    YOLO is used if the label should be a txt file
  4 – Start the labelling process

## Slide 31: 6. Data set creation
6.2.2 Label with labelimg – labeling description
  Start (4) by pushing the “Create\nRectBox” button
  Draw a rectangular around the traffic light that should be labelled
  Set the label according the traffic light status (red traffic light, yellow traffic light, green traffic light, red-yellow traffic light)
  After labelling save your image in the right format (VOC)

## Slide 32: 6. Data set creation
6.3 Creation of test and training data set
  Split the data in two groups and save them in different folders
  Training data set should be 70% of all images
  Test data set should be 30% of all images
  Always store the image and the related labelling file
  6.4 Integration of the data set into a repository
  Load both folders (test and training data set) into the project structure of your repository

## Slide 33: 7. CNN for traffic light detection
Learning objectives of this chapter:
  You can explain the current structure of the truck CNN for traffic light detection
  You know why the structure and the environment have a certain structure

## Slide 34: 7. CNN for traffic light detection
Explanation of the existing CNN structure
  xxxx

## Slide 35: References
  [1] GitHub, GitHub (logo). [Online]. Available: https://​github.com​/​
  [2] Google Colaboratory, Google Colaboratoy (logo). [Online]. Available: https://​colab.research.google.com​/​notebooks/​intro.ipynb